Daniel Keenan

FEA Project Elastic Waves

Prof. Bower

12/12/13

Introduction

The mechanism that causes a concussion is one of the least understood phenomena in injury diagnosis. One theory behind this devastating condition is that shear waves in the brain resulting from head impacts cause concussions. This theory arises from wave transference from the initial impact and the low tolerance of shear forces by brain tissue. These waves can be the most damaging to the brain and can lead to swelling of brain tissue resulting in headaches, blurry vision, and loss of consciousness. The potential for predictive modeling in this case is vast. A unique model for each patient that could simulate the impact that led to the concussion to determine the extent of the injury would be a tremendous help in diagnosing and treating concussions. For this to be accomplished, smaller steps must first be taken with simpler models. This project encompasses the effects of variable changes on the maximum stress experienced by the interior layer of a simple solid.
A simple model was used in this study that approximates a normal brain with a thin layer for the skull. In order to simplify calculations, the problem was set up as an axisymmetric simulation. A half-circle, seen in the figure below, was used to approximate the head. The circle was given a diameter of 15cm to approximate an average size head. A small layer was offset 0.3cm from the circumference of the circle to approximate the skull thickness. The outer layer was assigned an incompressible linear elastic material and the interior layer was assigned a Neo-Hookean material. Initial material properties were assigned to each section based on values found in literature to best approximate real tissue and bone. The brain was given a shear modulus of 0.9KPa and a density of 1.05 g/cm^3 and the skull was given an elastic modulus of 20.9GPa and a density of 1.9g/cm^3. Since the skull was assumed to be incompressible, the Poisson's ration was set to 0.49. In the assembly, a discrete rigid wire was added to contact the model at a velocity of 5m/s. Both the body and the wire were assigned xsymm boundary conditions for this simulation. Next, the contact parameters were set up with the wire as the master surface and the outer edge of the half-circle as the slave surface. In this simulation, the rigid surface moved toward the solid with the given velocity and after contact induced stresses along the skull layer and the brain layer.
Dimensionless groups were created to simplify the analysis and organize the data. From inspection it was determined that the stress in the solid is a function of the velocity of the rigid body, V0, the thickness of the skull, t, the radius of the head, r, the shear modulus, µ, the elastic modulus, E, the density of the brain, ρ1, and the density of the skull, ρ2. From these variables four dimensionless groups were created Π 1= ρ1/ρ2, Π 2= t/r, Π 3= V0/sqrt(μ/ρ1), and Π4=sqrt(E/ρ2)/sqrt(μ/ρ1). The max stress calculated in this study will be a dimensionless parameter, σ/μ.
Analysis
The solid was meshed and a simple mesh convergence study was conducted to determine the appropriate number of elements required to perform a useful analysis. To perform dynamic analysis hybrid elements were used to mesh the solid. Additionally, the elements were converted to quadratic because of the curved geometry of the solid. The first mesh tested was the basic mesh that ABAQUS generates without any refinement and then a succession of global refinements were added to the model until convergence was reached. At each mesh refinement level the max stress of the model at the first point of contact between the solid and the rigid body was recorded to check for convergence. The graph on the previous page shows the results of the convergence study. As illustrated by the graph, the mesh converges around 1000 elements at a stress of a little over 2MPa. The final mesh for the solid was chosen based on this criteria with a total of 1159 elements.
Mesh Convergence
Number of Elements
Stress (MPa)
After choosing an adequate mesh for the study, an experiment was set up to determine the changes in the max stress value of the brain section of the model as well as the stress distribution patterns in response to the dimensionless group parameters. First, the densities of the two layers were changed. The brain density was changed from 1.9g/cm^3 to 7.6g/cm^3 this corresponds to a change from 1 to 4 in the dimensionless group. Likewise, the skull density was changed from 0.25 to 4. Next, the shear modulus was varied from 300Pa to 600Pa in increments of 50 and the elastic modulus was tested over a range of 10Gpa to 50Gpa at an interval of 5. The thickness was varied from a value of 0.3cm to 2cm and the velocity was varied from 1cm/s to 20cm/s. At each value the maximum stress in the brain was recorded for comparison.
Results
By varying the values of Π1 the density of the skull and brain were changed as well. First, the skull density was kept constant and the brain density was varied. Then, the brain density was kept constant and the skull density was varied. On the graph below, the max stress is shown to increase with an increased density in the brain. It is also shown that the max stress in the brain increases with the density in the skull. Additionally, the stress pattern in the interior of the solid changed as well. The model is depicted with both low and high density at the same time point in the table below. The left image shows the brain with a lower density and the right image shows the brain with a higher density. A similar phenomena can be seen with the lower density skull and the higher density skull. The difference is much more pronounced in the brain model. Clearly the stress pattern dissipates faster in the higher density model stays around longer in the lower density model.
Skull Density
Density (g/cm^3)
Max Stress
Brain Density
Density (g/cm^3
Max Stress

Low Density Brain Model	High Density Brain Model

Low Density Skull	High Density Skull

In the simulation with the higher brain density, the wave propagated much slower through the solid. This resulted in a higher stress in the solid as well as a decreased stress resolution time in the solid. Functionally this is saying that the in a denser material the stress induced by an impact will be greater initially, but the lasting effects of the impact will be shorter. In the model with the higher density skull, the stress was transferred differently from the outer layer to the inner layer. This resulted in close to the same situation as the denser brain section.
The next group was the thickness group. For this study the radius was kept at a fixed length so only the thickness of the skull layer was varied. In the graph below, the results are shown for the different layer thicknesses. The max stress increased with an increase in thickness of the skull layer. The stress distribution on the on the skull layer showed a subtle change as well. When the boundary layer was thick as seen in the picture on the left the stress is more concentrated at the point of contact. However, when the skull layer is thin the stress spreads out along the skull layer.
Skull Thickness
Thickness (cm)
Max Stress
Thick Skull Layer	Thin Skull Layer

These results were much different than expected. When the skull layer was increased the stress did not act the same as when the skull layer was very thin. The stress stopped behaving as if there was a boundary layer and acted more like there was a uniform solid material. In the model with the thinner skull layer, the stress is shown to be guided along the edge similar to surface waves observed during earthquakes. However, in the thicker layer, the stress is more direct and penetrates close to the center line of the solid. This behavior looks similar to the stress patterns in the brain section. Additionally, the thicker layers induced much higher stresses than any other parameter change. The fundamental interaction between the shell layer and the internal solid changed when thickness of the skull approached the length of the radius. This decreased the size of the brain causing the boundary to have more of an effect on the internal solid.
After looking at the skull thickness parameter the velocity of the impact was changed to see its effect on the stress. At low velocities the stress value remained about the same, but when the impact speed was larger than 10cm/s the stress quickly rose. The slower impacts did not cause much strain in the elastic material and kept the stress very consistent. Looking at the pictures below the difference in stress pattern can be seen between slow head impacts and fast head impacts. The slower impact have a more direct stress pattern along the center while the faster impacts spread the stress along the boundary line between the brain and the skull layer.
Velocity
Velocity (cm/s)
Max Stress
This relationship between the velocity of the impact and the stress observed in the head is very straightforward. An increase in impact velocity increases the stress in the center of the circle. Faster wave speeds are possible with larger impact velocities and intuitively more damage occurs after a faster impact than a slower impact. Additionally, the stress pattern was altered when the velocity was increased. The slower impacts allowed for enough time for the material to have more localized stress patterns. Most of the stress can be seen right around where the impact occurs. When the impact speed increases there is less time for the solid to deform and so the stress pattern widens out and affects a much larger region of the brain. Also the faster speed corresponds to larger deformations that affect a larger region of the solid.
Slow Speed Impact	Fast Speed Impact

The last two parameters are the shear modulus and the elastic modulus. In the graphs below, the maximum stress actually decreases with increases in both elastic modulus and shear modulus. This displays the opposite trend of the other parameters. Increasing the shear modulus should allow larger waves speeds to occur. There was quite a bit of noise is the graphs for these two parameters. Unlike other variables the location of the max stress changed with some changes in the elastic and shear modulus. This may account for changes is the shear force throughout the solid.
Shear Modulus
Shear Modulus (Pa)
Max Stress
Elastic Modulus
Elastic Modulus (GPa)
Max Stress
Soft Brain	Stiff Brain

Soft Skull	Stiff Skull

The Soft brain in the table above does not seem able to support the same type of stress pattern as the stiffer brain. Conversely, the stiff skull was not able to transmit an ordered stress pattern like the soft skull as seen in table above. In the stiff brain picture, it can be seen that the max stress location has migrated away from the center line of the model is located closer to the boundary between the brain and skull layers. Most of the max stress locations were along the boundary between the interior solid and the skull layer. When the skull section stiffness was decreased that location moved to the center of the circle. Functionally, this could be attributed to the properties of the skull approaching the properties of the brain. This could result in a more homogenous material and negate some of the boundary behavior exhibited in previous simulations.
Discussion
During this study a multitude of different loading conditions were brought to attention. The change in parameters resulted in varied stress magnitudes, max stress locations, and stress distributions in the solid. The max stress experienced by the model ranged from 0.04 to 360,000. This large range is due to large changes in material properties and loading conditions. These differences in properties are not comparable to any fluctuations seen in nature or in the human body; however, results obtained from the study help to shed light on the relationship of loading, properties, geometry, and stress in a simplified model representing the brain and skull interface.
Some of the results in this study were contradictory to my opinion before doing this project. It looks like parameters that increase the speed of traveling waves in solids can actually produce lower stresses in the body. Moreover, the slower wave speeds created larger stresses. These fluctuations were generally small and were not on the same order as the change in material properties. Most of the material property changes were orders of magnitude larger than the resulting change in stress and would not be likely in nature.
The largest variations occurred when the geometry of the model was changed. Increasing the skull thickness layer changed the ratio of the brain material to the skull material and completely altered the physics of the impact. As the thickness became larger the brain section decreased proportionally and caused a much larger stress value in the center. This result was very interesting and unexpected.
In the context of brain issues, these results can be used to determine causes of injury by looking at the correlation of max stress location and the location of damaged tissue after injury. Also these results can be used to determine different materials that would be advantageous as wave guides to divert the force away from the head. This would then minimize the damage by distributing the force over a much larger area.